## Slide 1: Simulation of World’s Highest Jumping Robot
Junlin Chen
Sanskar Nalkande

## Slide 2: The Jumping Robot
Hybrid Tension-Compression Jumping Robot
  Methodology:
-DisMech DER Simulation
  Goal:
-Simulation matches real motion -Easy change of parameters and geometry

## Slide 3: Limb and Joint Construction
Dismech rod simulation in 3D
D = 1.45mm, E = 131GPa[2]
9 limbs and 9 joints(more to add)
Joint as single elastic body
0.03x0.03x0.3m in size[1]

## Slide 4: Force Application and Fixtures
Center edge of bottom cross is fixed
Force in the downward z direction uniformly distributed at top cross
Expected a constant application of force throughout time

## Slide 6: Work in Progress & Challenges
Z component force issue
Elastic bands(30.5x2mm)[1] addition
Ground contact rather than fixtures
Realistic way to apply force
Compute the total elastic energy stored[3]
Actuation?
Ground

## Slide 7: Possible Future Improvements
Recurve vs. normal bow
  Higher specific elastic energy
  Need to build from vertices rather than limbs
  Change natural curvature in DisMech

## Slide 8: Sources:
[1] E. W. Hawkes et al., "Engineered Jumpers Overcome Biological Limits via Work Multiplication," Nature News, Apr. 27, 2022.
[2] ACP Composites, "Solid Carbon Rod All Series PDS," No.49881, Oct.2019.
[3] M. Khalid Jawed, Class Lecture, Topic: "Networks of Beams." Module 17, University of California, Los Angeles. Oct, 2023.
[4] K. McLaughlin, A. Titus, “Elasticity of Thera-Band Resistance Band,” High Point University., High Point N.C., 2014.

## Slide 9: Thank you
Q&A Time